BEST MANAGEMENT PRACTICE ANALYSIS – AGRICULTURAL/RURAL

| BEST MANAGEMENT PRACTICE | AGENCIES TO ASSIST & CONSULT | POTENTIAL FUNDING SOURCES | INDICATORS OF PROGRESS | IMPLEMENTATION PRIORITY |
| --- | --- | --- | --- | --- |
|  |  |  |  | Short Term | Medium Term | Long Term |
| Conservation Easements Incentives to enter into conservation easements are not strong enough to convert their land out of production Mechanisms are currently in place to establish these easements; but landowners are not using them Main concern of landowners is effectively loosing their property rights on the land placed under the easement | Nature Conservancy Texas Parks and Wildlife Con-America Trust for Public Land | Funding is not typically available through tradition ag programs and is not considered an accepted conservation practice | Progress indicated by increase in acres enrolled in the watershed | Low | Medium | High |
| Fencing (Cross Fencing) Concerns for providing drinking water for cattle after fencing is installed Hardened access points can alleviate this There is a definite need for alternative water sources with this practice If the creek is fenced off and the middle of the creek is the property line, there is a fear of eventually losing the land near the creek (apparently legal action can be taken by someone else to gain that land) A fence is part of a buffer BMP if the land is grazed | USDA Natural Resources Conservation Service Texas State Soil and Water Conservation Board Kaufman-Van Zandt Soil and Water Conservation District | Funding from EQIP and 319 programs. | Progress indicated by linear feet installed and acreage protected. | High | Medium | Low |
| Filter Strips Currently a hard sell to landowners in the area due to high commodity prices (corn, maize, etc.) Incentive is not great enough to take the land out of production An increased incentive may be justified since this practice is so effective | USDA Natural Resources Conservation Service Texas State Soil and Water Conservation Board Kaufman-Van Zandt Soil and Water Conservation District | Funding from EQIP and 319 programs | Progress indicated by acres installed and treated | Low | Medium | High |
| Grade Stabilization Structures Typically a cost prohibitive practice (range from $3 to $10K each) Usually used in combination with grassed waterways Dam with pipes are typical in the Cedar Creek area but are typically more expensive than a concrete weir | USDA Natural Resources Conservation Service Texas State Soil and Water Conservation Board Kaufman-Van Zandt Soil and Water Conservation District | Funding from EQIP and 319 programs | Progress indicated by number of acres treated by the practice. | High | Medium | Low |
| Grassed Waterways Similar concerns as filter strips | USDA Natural Resources Conservation Service Texas State Soil and Water Conservation Board Kaufman-Van Zandt Soil and Water Conservation District | Funding with 319 and EQIP programs. | Progress indicated by acres installed and treated | Low | Medium | High |
| Critical Area Planting | USDA Natural Resources Conservation Service Texas State Soil and Water Conservation Board Kaufman-Van Zandt Soil and Water Conservation District | Funding with 319 and EQIP programs. | Progress indicated by acres installed and treated | Medium | High | High |
| Nutrient Management/ WQMP | USDA Natural Resources Conservation Service Texas State Soil and Water Conservation Board Kaufman-Van Zandt Soil and Water Conservation District | Funding from EQIP and 319 programs | Progress indicated by the number of acres the practice is applied to. | High | Medium | Low |
| Prescribed Grazing This practice ties to WQMPs and fencing BMP Educating landowners on the use of this BMP is critical; many landowners have the BMP in place, but do not use it properly Benefits of this practice are multi-pronged Increased nutrient removal if practice is used properly Grass production will likely increase with proper rotational grazing NRCS currently does not cost share this practice; TSSWCB includes this in their WQMPs | USDA Natural Resources Conservation Service Texas State Soil and Water Conservation Board Kaufman-Van Zandt Soil and Water Conservation District | Funding from EQIP and 319 programs. | Progress indicated by the number of acres applied to | High | High | High |
| Range/Pasture Planting Excellent practice for cropland to grassland conversion Unlikely to see this happen very much in near future due to high commodity prices; a more likely scenario is cropland to urban in the upper watershed There could also be a conversion of grassland back to cropland; it is happening in other parts of the state. | USDA Natural Resources Conservation Service Texas State Soil and Water Conservation Board Kaufman-Van Zandt Soil and Water Conservation District | Funding from EQIP and 319 programs | Progress indicated by the number of acres converted or planted | High | High | High |
| Septic System Maintenance | Texas AgriLife Extension Service Texas Commission on Environmental Quality Tarrant Regional Water District County Health Inspectors | SEPP (TCEQ), RC&D, TCEQ, 319 Program | Progress indicated by the number of units repaired and upgraded |  |  |  |
| Soil Testing | USDA Natural Resources Conservation Service Texas State Soil and Water Conservation Board Kaufman-Van Zandt Soil and Water Conservation District Trinity Neches Soil and Water Conservation Board (Henderson cnty) | Texas AgriLife Extension Service 319 programs | Progress indicated by the number of acres the practice is applied to | High | High | High |
| Stream Restoration Mitigation banking is the current trend in this practice Land that is put into mitigation banking may eventually convert to an easement of sorts Costs can be prohibitive for this practice Corps of Engineers permitting and possibly TCEQ permitting will likely be required | US Army Corps of Engineers- mitigation banking program Texas Commission on Environmental Quality Texas AgriLife Extension Service | Mitigation banking as a funding source. | Progress indicated by linear feet or miles of stream improved or restored. | Low | Medium | High |

Ideas:

- Develop fact sheets on economic benefits of practices

- Provide supplemental information on management practices to existing programs in the area; i.e. extension programs on grazing/ nutrients etc.

- May provide a speaker for the programs that highlights the water quality benefits of discussed practices along with economic returns that producer will realize