BEST MANAGEMENT PRACTICE ANALYSIS - URBAN

| BEST MANAGEMENT PRACTICE | AGENCIES TO ASSIST & CONSULT | POTENTIAL FUNDING SOURCES | INDICATORS OF PROGRESS | IMPLEMENTATION GOALS |
| --- | --- | --- | --- | --- |
|  |  |  |  | Short Term | Medium Term | Long Term |
| Ordinances Require public and private entities to reduce or eliminate the discharge of pollutant substances into watersheds Limit sedimentation from development projects, or mandate licensing or education for those who handle nutrients or pesticides. Allows opportunity to improve upon past pollution prevention performance Entities such as the US EPA have developed model ordinances for local governments to follow Will require publicity and education Must fund enforcement protocol Training must be provided to local enforcement authorities | Environmental Protection Agency Texas Commission on Environmental Quality Local Government – City, County North Central Texas Council of Government | Municipalities | Number of ordinances passed Number of enforcement officers trained |  |  |  |
| Low Impact Development | Environmental Protection Agency Texas Commission on Environmental Quality Local Government – City, County North Central Texas Council of Government | Environmental Protection Agency Texas Commission on Environmental Quality Developers | Development and adoption of voluntary or mandatory programs/ordinances |  |  |  |
| Construction Practices Sediment Fence Temporary barrier Limit the flow of silt and sediment from construction sites in which the soil is disturbed Adaptable to various conditions Requires proper installation for effectiveness Slows the drainage of water from construction area Must be inspected and repaired regularly | Environmental Protection Agency Texas Commission on Environmental Quality Local Government – City, County North Central Texas Council of Government | Texas Commission on Environmental Quality Developers | Number of developers advising on program. Securing of funding sources |  |  |  |
| Construction Practices Storm Drain Inlet Protection Prevent soil and debris from entering storm drain drop inlets Inexpensive Can be easily removed upon completion of project Effectiveness dependant on rate of growth Not aesthetically pleasing until growth begins | Environmental Protection Agency Texas Commission on Environmental Quality Local Government – City, County North Central Texas Council of Government | Texas Commission on Environmental Quality Developers |  |  |  |  |
| Porous Pavement Permeable surface that allows the passing of stormwater though an underlying stone reservoir Most commonly used as parking area surface and mitigates the flux of stormwater from parking surfaces in a rain event Reduces pollutants from stormwater runoff Installation and replacement costs are high Short life span in high traffic areas Siting requirements are strict |  | Texas Commission on Environmental Quality Pavement Company |  |  |  |  |
| Highway Projects Right of Way Maintenance Watershed counties are tasked with maintaining roadside ditches and unincorporated storm drains Removal of trash and other debris on a regular basis Mowing and maintenance of landscaping Removal of clogging materials from ditches and drainages can help prevent flooding Proper disposal of trimmings and debris must be followed | Texas Department of Transportation County Commissioners Municipalities | Texas Department of Transportation County Commissioners Municipalities | Identification of priority areas |  |  |  |
| Highway Projects Roadside Seeding Seeding is used to control runoff and erosion on disturbed areas by establishing perennial vegetative cover from seed Reduces erosion and sediment loss and provides permanent stabilization Easy to apply to large areas Low labor and material cost compared to planting or vegetation blankets Effectiveness dependant on rate of growth | Texas Department of Transportation County Commissioners Municipalities | Texas Department of Transportation County Commissioners Municipalities | Identification of priority areas |  |  |  |
| Rainwater Harvesting Can reduce the volume of stormwater, reduce erosion, and storm sewer impact Reduces utility bills May have difficulty with approval from homeowners associations due to aesthetic concerns | Texas AgriLife Extension Texas Water Development Board Texas Commission on Environmental Quality | Texas Commission on Environmental Quality Texas Water Development Board Municipalities Counties Private grants | Number of systems installed |  |  |  |
| Bioswales Open, vegetated channel that collects and diverts the flow of storm water to a desired location Widely applicable Suited for highway or residential roads due to linear designs Aesthetically pleasing Cannot treat a large drainage area Thick vegetation is needed for swales to function properly May attract breeding mosquitoes Must be designed properly to be effective | Texas AgriLife Extension | Texas Commission on Environmental Quality Municipalities Counties Private grants | Progress toward number of feet of bioswales implemented |  |  |  |
| Constructed Wetlands Flood control Pollutant removal Channel erosion protection Aesthetic value Design and plant selection must have longevity Nutrient release during non growth season | Environmental Engineering Firms Tarrant Regional Water District | Environmental Protection Agency Texas Commission on Environmental Quality | Number of acres of constructed wetlands implemented |  |  |  |
| Nutrient Management (Low/Phosphorus Free Fertilization) Education and outreach to control the effects of landscaping and lawn care practices on stormwater Voluntary program/difficult to enforce Allows citizen education through participation Must solicit participation of local landscape companies to stock correct fertilizers and pesticides | Texas AgriLife Extension Municipal Parks and Recreation Departments Homeowners Golf course operators Retail Stores | Texas Commission on Environmental Quality Municipalities Counties | Establishment of no fertilizer set backs around reservoir Number of homeowner contacts |  |  |  |
| Storm Drain Inlet (sand filters) Pollutant removal Can be used in highly urbanized settings or when topography or geology disallows other BMPs Can be underground or as part of road construction to minimize visual impact Requires frequent maintenance Cannot be used to treat large drainage areas | Environmental Engineering Firms Municipalities |  | Number of installations |  |  |  |
| LID Ribbon Curb Eliminates gutters and works to lessen stormwater runoff | Developers Cities | Developers | Passing of ordinance requiring installation on new developments |  |  |  |
| Illegal Dumping Prevention Improves water quality Improves aesthetics Increases property values Reduces order and nuisance pest problems Public participation creates “ownership” of issue Enforcement typically through fines, jail, or community service Resources needed to compliment investigation | Texas Commission on Environmental Quality Counties Municipalities | Texas Commission on Environmental Quality Counties Municipalities | Clean up of established dumping sites, signage, dedicated community clean-up days |  |  |  |
| Storm Drain labeling Volunteer-based or paid city worker-based Storm drains discharge directly into streams and watersheds Prevention of dumping chemicals and organic matter into storm drains Easy to implement Increases public awareness of storm sewer watershed link Deters littering, illegal dumping, and nutrient infusion | Texas Cooperative Extension Municipalities Counties Schools Service clubs Youth organizations | Counties Municipalities | Number of Storm drains stenciled |  |  |  |